## Slide 1: SAEISS Aero Design Challenge 2020, Regular Class SASTRA Deemed To Be University, Thanjavur Technical Presentation
By
Team Udyat ADC2020114

## Slide 2: Project Planning
Project approach
To practically apply our Theoretical Knowledge combined with our thought processes. Mimicking a fully functional aerospace engineering firm.
Project Timeline
Design Approach
Conceptual Design
Detailed Design
Team Registration and Memberships
Initial Discussions
Literature and Design Report Study
Sub-System Allocations and Working
Design Report completion and Submission
Fabrication /Technical Preparation
Test Flight and changes
Order of Components and Materials

## Slide 3: SAE AERO-DESIGN COMPETITION ROADMAP
2019-2020
2019
August
Understanding problem-statement
September
Attending workshop
Basic calculations
Semester exams
Material selection
Dealers contact
December
Modelling
Design report
2020
January
Final design report
Scale down model
February
Fabrication
Technical presentation
Team meetings
Weight estimation
October
November
TEAM UDYAT
* Literature study is a part of all months

## Slide 4: Design Approach
Conceptual Design
Detailed Design
3-D drag analysis
Structural Analysis.
Power Plant.
Material Selection.
Fabrication Feasibility.

## Slide 5: Procedure
UDYAT plane
Weight estimation
Wing design
Empenage
Fuselage
C.G location
Landing gear

## Slide 6: Requirements and Constraints ( Include Sae plane)
Ss
SAE
Requirements and Constraints
Problem statement
Total Length <170 inches .
2kg <Weight<5kg
Fabrication Feasibility
Cost
Time
Propulsion System
FRP and Lead Prohibited
Total Take off distance 200ft.
Total Landing distance 400ft.
Additional Constraints

## Slide 7
SAE
Requirements and Constraints
Additional Constraints
Problem statement
Total Length <170 inches .
2kg <Weight<5kg
Fabrication Feasibility
Cost
Time
Total Take off distance 200ft.
Total Landing distance 400ft.
Propulsion System
FRP and Lead Prohibited

## Slide 8: Configuration Selection and Trade Studies
Evaluation Criteria:
Induced drag
Weight Reduction
Near Elliptical Distribution
Manufacturability
Evaluation Criteria:
Reduced Parasite drag
Reduced rudder-induced roll
Free of fuselage wake
Reduced Cantilever stress
Evaluation Criteria:
Prevents Ground looping
A
Ad
Evaluation Criteria:
Less impact during landing
Laterally stable
Smooth finish of Fuselage
Ease of Wing-Fuselage Assembly.
Fuselage Evaluation Criteria:
Innovation
Reduced Influence of Wing wake on Tail
Ease of manufacturing

## Slide 9: Vehicle Sizing
Lift Requirement
Payload Requirement
Avionics Requirement
Volume Coefficients
Airfoil Selection
Wing Dimensions
Fuselage Dimensions
Horizontal Stabilizer Dimensions
Vertical Stabilizer Dimension
Vehicle was sized based on competition requirements, meanwhile considering the aerodynamic characteristics and structural integrity.
Aerodynamic parameters and Fabrication feasibility were considered, iterated and necessary design changes were made.

## Slide 10
Wing configuration
Wing planforms
Wortman fx-63-137
E-423
S1210
S1223
Airfoils
Wing specifications
Wing

## Slide 11
Fuselage
INNOVATION:
The purpose of the step, it is claimed, is to allow some of the displaced air to fall into a pocket behind the step and become part of the airfoil shape as a trapped vortex. This purportedly prevents separation and maintains airflow over the surface of the airfoil. A similar step is made after the diverging part of fuselage to attach the flow and reduce the slope of decrease in lift.
Fuselage front view
Fuselage side view

## Slide 12: Innovation
The purpose of the step, it is claimed, is to allow some of the displaced air to fall into a pocket behind the step and become part of the airfoil shape as a trapped vortex. This purportedly prevents separation and maintains airflow over the surface of the airfoil. A similar step is made after the diverging part of fuselage to attach the flow and reduce the slope of decrease in lift.

## Slide 13: Vehicle Sizing
Performance Parameters
Maximum Lift Co-efficient
Maximum L/D Ratio
Wing-Loading
Aerofoil Selection
(Wind-Turbine blades)
Optimisation of Aspect Ratio
Informal Optimisation of Cruise-Velocity
WING-DIMENSIONS

## Slide 14
Avionics Requirements
Manufacturing Ease
Payload Requirements
Fuselage Dimension
Volume Coefficients
Wing- Dimensions
Aerofoil
Vertical and Horizontal Stabiliser
Vehicle was sized based on competition requirements, meanwhile considering the aerodynamic characteristics and structural integrity.
Aerodynamic parameters and Fabrication feasibility were considered, iterated and necessary design changes were made.

## Slide 15
Airfoil
Aspect ratio
Wing Dimensions
Cruise velocity
Max L/D ratio
Fuselage dimensions
Avionics requirement
Performance parameters
Wing loading
Max. lift coefficient
Volume coefficients
Manufacturing Ease
Payload requirements
Stabilisers
Vehicle Sizing

## Slide 16
WING
Required Lift L=5.75Kg
Assumed Speed Vc=10m/s
Airfoil= S1223
For Wing: CLmaxw= Clmax * 0.95= 2.177
CL ideal = Cl ideal *0.95= 1.0973
For Aircraft: CLAmax = 2.177* 0.9=1.95
CLA ideal= 1.0973*0.9= 0.98
Airfoiltools.com
Lift = ½* 𝜌∗𝑉𝑐2∗𝑆∗𝐶Lmax.
56.4075= .5*1.225* 100* S* 1.95
Span area (S)= .4722 m2. = 732in2.
Literature Study and Optimisation of Aspect Ratio.
A.R= 7
Span Length (b)= 71.58in
Mean Aerodynamic Chord MAC = 10.22in
Landing Distance
𝑆𝑔=1.21∗(𝑊/𝑆)/ (𝑔∗𝜌∗𝐶𝐿A𝑚𝑎𝑥∗𝑇/𝑤)
T/W= (1.21*20)/ (32.2*0.002377*1.95*200) = 0.81.

## Slide 17: Tail-Section
Horizontal Stabilizer
(PITCH STABILITY)
Literature Study NACA 0009, Volume Coefficient 0.6
Vertical Stabilizer
(DIRECTIONAL STABILITY)
Literature Study Volume Coefficient 0.05
Formal Optimisation of Span area
130 sq. in
ARh=(2/3)ARw=4.66
Span length=24.61 in
chord=5.27 in
Elevator chord=2 in
Elevator length=24.61 in
Vv =. (𝑆𝑣∗𝐿𝑣)𝑆𝑤∗𝑏
Formal Optimisation of Span area
83 sq. in
ARh=2.5
Height=12 in

## Slide 18
Empennage
Horizontal & vertical Stabilizer
Tail cone side view
Tail isometric view
Airfoil-NACA0009

## Slide 19
Landing gear

## Slide 20: Centre of Gravity and stability
Xflr
COG location using XFLR5: 1.997(from MAC of 10.1 in)
Analytical
Xnp = 3.027 inches (for 10.1 inches MAC).
We chose the mid value of Stability margin which is 0.10.
Xcg = 2.017 inches (from MAC of 10.1 inches).

## Slide 21: Stress analysis and Material Selection
Distance Between Ribs:
Iterative Process
𝐶𝑝=(𝑃𝑜−𝑃𝑎)/ 5∗𝜌∗𝑉𝑐2.
𝑃𝑜−𝑃𝑎= 350 Pa
 | Density, g/cc | Strength, MPa | Specific strength | Youngs Modulus, GPa | Flexural Modulus, GPa | Elongation, % | Fatigue Mpa
Balsa Wood | 1.63 | 30 | 18.40 | 3.71 | NA | NA | 
Depron | NA | NA | NA | NA | NA | NA | 
Corrugated plastic | NA | NA | NA | NA | NA | NA | 
Elasto foam | NA | NA | NA | NA | NA | NA | 
FRP | 1.5 | 85 | 56.67 | 3.4 | 3.6 | 5 | 
PLA | 1.25 | 65 | 52.00 | 3.5 | 4.5 | 12 | 
ABS | 1.08 | 55 | 50.93 | 3.1 | 2.5 | 20 | 
Nylon 6 | 1.12 | 70 | 62.50 | 3.1 | 2.6 | 35 | 
Nylon 66 | 1.14 | 90 | 78.95 | 2.9 | 2.4 | 45 | 
PEEK | 1.3 | 95 | 73.08 | 4 | 3.8 | 45 | 
Torlon | 1.42 | 170 | 119.72 | 4.9 | 5 | 15 | 
Al 7075 T6 | 2.7 | 570 |  | 71GPa |  | 10 | 300
Material Selection Trade-Off

## Slide 22: Empirical Results

## Slide 23: Lessons Learnt
We have the aerodynamic knowledge, the structural materials, the powerplants, and the manufacturing capacities to perform any conceivable miracle in aviation. But miracles must be planned, nurtured, and executed with intelligence and hard work”.
- Glenn L. Martin, aviation pioneer and manufacturer, 1954.
Checking the availability of necessary components before coming to design conclusions.
Fabrication and Manufacturing required a yet another different set of skill.
Time Management
Finance management

## Slide 24: Queries?